## Slide 1: Metaforge Repeat Order Hardness 應測數目減半

## Slide 2: 1. Review Hardness Performance on Repeat Order in the past year
It is recommended Core Hardness Sampling is decreased to 8 pcs.
藉由以下取樣區間內的數據得知, supplier 控制硬度能力已趨穩定, 故建議core hardness檢驗支數由15 pcs減為8 pcs甚或更少.
Recommendation is based on following statistic:
下為取樣區間的統計數據呈現
取樣區間 Duration: Apr. 2018 ~ May.2019
取樣範圍
18 Parts(19 Orders)
Heat treatment on part:
  SAE J429 Gr-5: 17 parts
  SAE J429 Gr-8: 1 part

## Slide 3
PO | PN | Date | Qlab report Number | Standard | Result | Note
23342921 | HJW5W | 2018/6/25 | R18090448 | HRC 25~34 | 30~32 | 
2334140 | HK6KY | 2018/7/20 | R18070903 | HRC 25~34 | 30~31 | 8 pcs
2334293 | HJW68 | 2018/7/31 | R180741252 | HRC 25~34 | 27~29 | 
2335142 | HJWPP | 2018/7/31 | R18071253 | HRC 25~34 | 30~31 | 
2336759 | HK639 | 2018/7/31 | R18071257 | HRC 25~34 | 30~31 | 
2327029 | HK63C | 2018/7/31 | R18071259 | HRC 25~34 | 28~32 | 
2334140 | HK6KY | 2018/7/31 | R18071255 | HRC 25~34 | 30~31 | 7 pcs
2298648 | HJWPQ | 2018/8/3 | R18071258A01 | HRC 33~39 | 35~37 | Gr-8
2335142 | HJWJ9 | 2018/8/8 | R18080352 | HRC 25~34 | 31~32 | with 2342279
2334429 | HK6T0 | 2018/8/8 | R18080360 | HRC 25~34 | 27~29 | 
2298649 | HJWP6 | 2018/8/13 | R18080570 | HRC 25~34 | 29~31 | with 2343875, 11 pcs.
2346341 | HJW6P | 2018/9/14 | R18090450 | HRC 25~34 | 30~32 | 
2327029 | HJW66 | 2018/9/19 | R18090837 | HRC 25~34 | 31~31 | 
2335142 | HK6KW | 2018/10/17 | R18100677 | HRC 25~34 | 26~28 | 
2298648 | HJWPQ | 2018/10/18 | R18100681 | HRC 33~39 | 37~38 | Gr-8
2317799 | HJWJK | 2018/11/13 | R18110428 | HRC 25~34 | 29~31 | 
2347263 | HMHV0 | 2018/11/13 | R18110457 | HRC 25~34 | 29~30 | 
2354903 | HJWJ8 | 2018/12/20 | R18120868 | HRC 25~34 | 33~35 | With 2333986 HRC 33~34, 1 pc failed at HRC 35
2357698 | HJWJ9 | 2019/1/17 | R19010700 | HRC 25~34 | 30~32 | 
2357698 | HJWMP | 2019/1/18 | R19010685 | HRC 25~34 | 30~32 | 
2357698 | HK639 | 2019/1/18 | R19010704 | HRC 25~34 | 28~31 | 
2359829 | HJW62 | 2019/2/14 | R19020254 | HRC 25~34 | 30~32 | 
2358711 | HJWPQ | 2019/2/14 | R19020253 | HRC 33~39 | 37~38 | Gr-8

## Slide 4
23342921 HJW5W
2334140
HK6KY
39
37
35
33
31
29
27
25
2334293HJW68
2335142HJWPP
2336759
HK639
2327029
HK63C
2298648
HJWPQ
2335142HJWJ9
2334429
HK6T0
2298649
HJWP6
2346341
HJW6P
2327029
HJW66
2335142
HK6KW
2298648
HJWPQ
2317799
HJWJK
2347263
HMHV0
2018/12/20, 2336759
HK639, HRC 33~34
1 pc oversized at HRC 35
2357698
HJWJ9
2357698
HJWMP
2357698
HK639
2359829
HJW62
2358711
HJWPQ
Gr-5 硬度落點
Gr-8 硬度落點